## Slide 1: Machine Learning Vigilance for CAN Bus
Real-Time Anomaly Detection for CAN Bus Protection for Enhanced Automotive Cybersecurity
Team Name : CAN Vigilance
2200049004
2200049010
2200049137
2200049143
KPIT K-Impact

## Slide 2: Introduction
Increasing Connectivity: Modern vehicles are becoming more connected, enabling advanced features and over-the-air updates.
Vulnerability of CAN Bus: The Controller Area Network (CAN) bus, which connects critical Electronic Control Units (ECUs) in the vehicle, lacks built-in security features like encryption, message authentication, or access control.
Cyberattack Risks: Due to this lack of security, the CAN bus is vulnerable to various cyberattacks such as:
Spoofing: Malicious messages pretending to come from legitimate ECUs.
Replay Attacks: Unauthorized retransmission of recorded messages
Denial-of-Service (DoS): Flooding the bus with excessive traffic, causing system failure.
Fuzzing: Injecting malformed data to exploit vulnerabilities in ECUs.
Potential Impact: A successful cyberattack on the CAN bus can lead to severe consequences, including unintended acceleration, disabling safety systems (like airbags or brakes), or disrupting vehicle control systems, endangering both the vehicle occupants and other road users.
Need for Solution: There is an urgent need for a robust, real-time anomaly detection system to monitor and protect the CAN bus from such malicious attacks to ensure vehicle safety and cybersecurity.

## Slide 3: Objective
To develop a Real-Time Anomaly Detection System for the CAN bus in vehicles, leveraging Machine Learning (ML) techniques to enhance automotive cybersecurity. This system aims to continuously monitor CAN bus traffic, analyzing messages exchanged between Electronic Control Units (ECUs) to detect any unusual patterns or behaviors that could indicate a potential cyberattack. By training an ML model on normal vehicle communication data, the system will establish a baseline of legitimate CAN bus traffic, allowing it to identify anomalies in real time. The project will focus on detecting various types of attacks, including spoofing, where malicious messages appear to come from legitimate ECUs; replay attacks, involving unauthorized retransmission of recorded messages; Denial-of-Service (DoS) attacks, which flood the bus with excessive traffic; and fuzzing, which involves injecting malformed or random data to discover vulnerabilities. Upon detecting anomalies, the system will trigger immediate alerts or corrective actions to prevent vehicle malfunctions or safety risks. Additionally, the system will be designed to adapt to new data and evolving attack strategies, ensuring continuous and reliable protection against emerging threats.

## Slide 4: Block Diagram
Vehicle CAN Bus
CAN Sniffer Hardware
Data Preprocessing
Anomaly Detection & Alert
ML Model

## Slide 5: Reference
https://www.researchgate.net/publication/383901284_Unsupervised_Anomaly_Detection_for_Automotive_CAN_Bus_on_the_Intel_Loihi
https://www.researchgate.net/publication/380545048_Anomaly_Detection_of_CAN_Bus_Messages_Using_a_Deep_Neural_Network_for_Autonomous_Vehicles?_tp=eyJjb250ZXh0Ijp7ImZpcnN0UGFnZSI6InB1YmxpY2F0aW9uIiwicGFnZSI6InB1YmxpY2F0aW9uIn19
https://dr.lib.iastate.edu/server/api/core/bitstreams/6420dc37-5084-4b25-bbb2-d7bf14419616/content

## Slide 6
Thank you